## Slide 1: Session 3: DC Motor,Transistor, Flyback Diode, and Other Parts

## Slide 2: What We Learn Today
How to use a DC Motor
  DC Motor
  Transistor
  Flyback Diode
Other Electric Parts
  Solenoid
  Relay
MP3 Player
MINI LCD Display

## Slide 3: Session 3.1: How to Use a DC Motor

## Slide 4: DC Motor
Just connecting a DC motor to the Arduino’s digital output doesn’t work.

## Slide 5: DC Motor
Why?
Arduino can’t supply enough electric current to drive a DC motor (the Arduino’s digital output can supply max 20mA).

## Slide 6: DC Motor
Why?
Arduino can’t supply enough electric current to drive a DC motor (the Arduino;s digital output can supply max 20mA).
We need an external power supply and
control it by the Arduino’s digital/analog output.

## Slide 7: Transistor
Transistors can be used to amplify the electric current.
A transistor has 3 legs.
  Emitter
  Collector
  Base
If the current flows from the base to the emitter, the transistor amplifies the current from collector to emitter.
Image: https://en.wikipedia.org/wiki/Transistor#/media/File:Transistor_Simple_Circuit_Diagram_with_NPN_Labels.svg (license: CC-BY-SA 3.0).

## Slide 8: Transistor
The pin order of PN2222A transistor is assigned as shown on the right.
The pin order differs among transistors.
Be sure to check the pin order of your transistor.
C
B
E

## Slide 9: Transistor
Let’s build a circuit with a transistor!

## Slide 10: Transistor
The digital output #9 is connected to the ‘base’ pin of the PN2222A transistor (via a 330Ω resister）, then it is connected to the ground via the emitter.
E
B
C

## Slide 11: Transistor
The power is supplied from the 5v pin and drawn to the collector (then, going to the GND via the emitter). The amount of the electric current of this route is controlled by the output from the digital output that goes through the base.
E
B
C

## Slide 12: Transistor
You can use a transistor for various purposes.
For example, a LED strip normally requires more electric current, and may also require higher voltage.
Using a transistor, you can control the on/off by the digital output and brightness by PWM.
image: https://pixabay.com/p-2103022/?no_redirect (Pixabay License, Free for commercial use. No attribution required)

## Slide 13: DC Motor
You can also use an external power source (just share the GND).

## Slide 14: DC Motor
Now we learned how to control a a DC Motor, but what is this?

## Slide 15: Flyback Diode
This is a diode.
We already used one. LED = Light Emitting Diode.
Electric current can flow only from the anode side to the cathode side.
Anode
Cathode

## Slide 16: Flyback Diode
Then, why do we need a diode here?

## Slide 17: Flyback Diode
A motor has magnetic coils inside.
When the switch is closed, the electric current flows through the magnetic coil.

## Slide 18: Flyback Diode
What happens when the switch is set off?
  Magnetic coils have the characteristic to resist the change of the current.
  If the current increases, a magnetic coil opposes by
  self-induced EMF: Vr = -L * ΔI/Δt
  This means ”if the electric current drops down a lot suddenly, self-induced EMF will be very large”.
This can cause a very large voltage (even more than 5 to 20 times than the original voltage) , and it can break your circuit (including your Arduino!!).
A flyback diode can be used to avoid such a situation.

## Slide 19: Flyback Diode
The images are from https://upload.wikimedia.org/wikipedia/commons/7/76/FlybackExample.GIF and https://upload.wikimedia.org/wikipedia/commons/f/f8/Lichtbogen_3000_Volt.jpg . (license: CC-BY-SA 3.0 for both images)
an electric arc
Note that the polarity changes but the electric current flows to the same direction.

## Slide 20: Flyback Diode
This is why we need a flyback diode.

## Slide 21: Flyback Diode
While the DC motor is active, it stores the energy.
The electric current doesn’t go through the blue route, as the electric current can’t flow from cathode to anode.
+
-
+
-

## Slide 22: Flyback Diode
While the DC motor is stopped, it releases the stored energy and tries to keep the same flow of the electric current as possible.
However, the electric current won’t go through the transistor, as the base current is not given.
+
-
22
+
-
However, it can go through the flyback diode, as now it is the motor that supply the electric current.
Thus, the sudden large voltage can be avoided and the circuit (including your Arduino!) can be protected.
This electric current will be stopped when the motor already consumed all the stored energy.

## Slide 23: Flyback Diode
While the DC motor is stopped, it releases the stored energy and tries to keep the same flow of the electric current as possible.
However, the electric current won’t go through the transistor, as the base current is not given.
+
-
However, it can go through the flyback diode, as now it is the motor that supply the electric current.
Thus, the sudden large voltage can be avoided and the circuit (including your Arduino!) can be protected.
This electric current will be stopped when the motor already consumed all the stored energy.

## Slide 24: Transistor
How much electric current should be provided for the base-emitter?
Let’s say we use the 3V for the motor and we want to provide 500mA for the motor.
Let’s see the datasheet!
There would be something similar to the right figure.
Image: created by the author, following TOSHIBA. 2SC2120 Datasheet.
COLLECTOR-EMITTER VOLTAGE VCE (V)
0
1
2
3
4
5
6
200
400
600
800
1000
COLLECTOR CURRENT IC (mA)
COMMON EMITTER
Ta = 25℃
IC - VCE
IB = 1mA
0
6
7
8
3
2
4
5

## Slide 25: Transistor
We use the 3V for the motor and we want to provide 500mA for the motor.
First, check the ‘3V’ at the X-axis.
COLLECTOR-EMITTER VOLTAGE VCE (V)
0
1
2
3
4
5
6
200
400
600
800
1000
COLLECTOR CURRENT IC (mA)
COMMON EMITTER
Ta = 25℃
IC - VCE
IB = 1mA
0
6
7
8
3
2
4
5
Image: created by the author, following TOSHIBA. 2SC2120 Datasheet.

## Slide 26: Transistor
We use the 3V for the motor and we want to provide 500mA for the motor.
Then, check the 500mA on the Y axis.
COLLECTOR-EMITTER VOLTAGE VCE (V)
0
1
2
3
4
5
6
200
400
600
800
1000
COLLECTOR CURRENT IC (mA)
COMMON EMITTER
Ta = 25℃
IC - VCE
IB = 1mA
0
6
7
8
3
2
4
5
Image: created by the author, following TOSHIBA. 2SC2120 Datasheet.

## Slide 27: Transistor
The point (3v, 500mA) is at the middle of the 4mA line and the 5mA line.
Hence, we need to provide about the 4.5mA to the base.
The Arduino’s digital output is 5V.
We use V=IR again here! 5 = 0.0045 * R
R = 5 / 0.0045 = 1111.11…
We can use one 1k ohm resistor and one 200Ω resistor (1.2k in total).
Image: created by the author, following TOSHIBA. 2SC2120 Datasheet.
COLLECTOR-EMITTER VOLTAGE VCE (V)
0
1
2
3
4
5
6
200
400
600
800
1000
COLLECTOR CURRENT IC (mA)
COMMON EMITTER
Ta = 25℃
IC - VCE
IB = 1mA
0
6
7
8
3
2
4
5

## Slide 28: Ardestan Exercise #1
Create a program and a circuit that control the rotation speed of a DC motor by a potentiometer.

## Slide 29: What We Learned So far
How to use a DC Motor
  DC Motor
  Transistor
  Flyback Diode
Other Electric Parts
  Solenoid
  Relay
MP3 Player
MINI LCD Display

## Slide 30: Session 3.2: Other Electric Parts

## Slide 31: Solenoid
Solenoids are actuators that are electromagnetically drive.
There are various kinds of solenoids (push-pull, rotary, water valve, etc.)
The left figure is an example of a small push-pull solenoid.
Image: https://www.sparkfun.com/products/11015 (CC BY 2.0)

## Slide 32: Solenoid
Solenoids can be used in the same manner as DC motors.

## Slide 33: Solenoid
Explain Why we need a diode here.

## Slide 34: Solenoid (Push-Pull)
Click this URL to see the video.
https://www.youtube.com/watch?v=W9j6ZRsOUrI

## Slide 35: Solenoid Example (Water Valve)
Click this URL to see the video.
https://www.youtube.com/watch?v=tnPnwET4x9k&feature=emb_logo

## Slide 36: Relay
A relay is a switch that can be electrically operated.
Electromagnet is used for switching.
Check how much is min and max voltages to utilize.
Always check the data sheet!
Image: https://www.sparkfun.com/products/100 accessed on Oct- 21-2016. (License: CC BY-NC-SA 3.0)

## Slide 37: Relay
Relay is a mechanically controlled switch, which uses an electromagnet inside.
When the electric current flows in to the electromagnet, it can switch another circuit on/off or between two circuits in this case.
The left figure is the latter kind
Image: from Wikimedia Commons, https://upload.wikimedia.org/wikipedia/commons/0/05/Relay_Parts.jpg (public domain)

## Slide 38: Relay
There exists several kinds of relays.
  SPST – Single-Pole Single-Throw
  SPDT – Single-Pole Double-Throw
  DPST – Double-Pole Single-Throw
  DPDT – Double-pole Double-Throw
Image: from Wikimedia Commons, https://commons.wikimedia.org/wiki/File:Relay_symbols.svg (public domain)

## Slide 39: Relay
Here is an example circuit to control a relay

## Slide 40: Relay
Explain why we need a diode here.

## Slide 41: Relay
However, there exist various relay modules, which is quite easy to use.

## Slide 42: Ardestan Exercise #2
Create a program and a circuit that control a push-pull solenoid by a button.

## Slide 43: Ardestan Exercise #3
Create a program and a circuit that use a relay to switch on/off another circuit with a LED and a resistor by a button.

## Slide 44: What We Learned So far
How to use a DC Motor
  DC Motor
  Transistor
  Flyback Diode
Other Electric Parts
  Solenoid
  Relay
MP3 Player
MINI LCD Display

## Slide 45: Session 3.3: MP3 Player and MINI LCD Display

## Slide 46: MP3 Player
Create a below circuit
Be sure that the direction of the DFPlayer Mini and the connection are all correct. Otherwise, you can break the DFPlayer Mini.
1kΩ

## Slide 47: MP3 Player
Prepare a Micro SD.
  Put the MP3 files into the SD card.
Name your files like 00XX_[song title].mp3, For instance,
  0001_song_title.mp3 0002_song_title.mp3 0003_song_title.mp3
Creates a folder ‘mp3’ under the root directory of your SD card.
  /mp3/0001_song_title.mp3 0002_song_title.mp3 0003_song_title.mp3 DO NOT CREATE ANYTHING ELSE IN THE SD CARD!
  Otherwise, it may not work as expected.

## Slide 48: MP3 Player
Mac users should execute “dot_clean /Volumes/<SDVolumeName>” in the Terminal application, to remove unnecessary files in the SD card (always do this!).

## Slide 49: MP3 Player
The dfplayer_mini object controls the DFPlayer Mini module.
  When it received an integer value at the left inlet, it is used as the song number to play back.
  An integer value received at the right inlet specifies the playback volume.
  There are also the features such as, pause/start, volume up/down, next/previous. See more details for the help file.

## Slide 50: MP3 Player
To use the dfplayer_mini object, install the DFRobotDFPlayerMini library from the Library Manager.
Then, unzip the file dfplayer_mini and place the directory inside your project folder.

## Slide 52: Ardestan Exercise #4
Create a mp3 player with three buttons
  start playing when the left button is pressed.
  pause when the middle button is pressed.
  skip to the next song when the right button is pressed.

## Slide 53: Mini LCD Display
Ardestan also provides an object for lcd displays.
Currently only supports an LCD display with the i2c interface (the LCD controller should be HD44780-compatible; most LCD displays uses this).
Image: https://www.sparkfun.com/products/9395 (CC BY 2.0)

## Slide 54: Mini LCD Display
Connect the Mini LCD Player to the Arduino as below

## Slide 55: Mini LCD Display
The lcdi2c_hd44780 object can be used to control a HD44780-compatible i2c LCD display.
The object will display string/integer/float values (that are received at the left-most inlet) at the current cursor position of the LCD display.
See the help file for more details.

## Slide 56: Mini LCD Display
To use the lcdi2c_hd44780 object, first install the hd44780 library from the Library Manager.
Then, unzip the file: lcdi2c_hd44780 to your project directory.

## Slide 58: Ardestan Exercise #5
Create a mp3 player with a mini LCD display.
  Display a current song number of the mp3 player in the LCD display (show some message like “Song No: 2”) at the first row of the display.
  Let the play back volume be controlled by a potentiometer. Display the current volume at the second row of the display.

## Slide 59: What We Learned Today
How to use a DC Motor
  DC Motor
  Transistor
  Flyback Diode
Other Electric Parts
  Solenoid
  Relay
MP3 Player
MINI LCD Display